- ESPHome Configuration ▸
- Sensor Component ▸
- SCD30 CO₂, Temperature and Relative Humidity Sensor
# SCD30 CO₂, Temperature and Relative Humidity Sensor
The scd30 sensor platform allows you to use your Sensirion SCD30 CO₂ (datasheet) sensors with ESPHome. The I²C Bus is required to be set up in your configuration for this sensor to work.

# Example configuration entry
sensor:
  - platform: scd30
    co2:
      name: "Workshop CO2"
      accuracy_decimals: 1
    temperature:
      name: "Workshop Temperature"
      accuracy_decimals: 2
    humidity:
      name: "Workshop Humidity"
      accuracy_decimals: 1
    temperature_offset: 1.5 °C
    address: 0x61
    update_interval: 5s
## Configuration variables:
- co2 (Optional): The information for the CO₂ sensor.
  - All options from Sensor.
- temperature (Optional): The information for the Temperature sensor.
  - All options from Sensor.
- humidity (Optional): The information for the Humidity sensor.
  - All options from Sensor.
- temperature_offset (Optional, float): Temperature and humidity offsets may occur when operating the sensor in end-customer devices. This variable allows the compensation of those effects by setting a temperature offset.
- automatic_self_calibration (Optional, boolean): Whether to enable automatic self calibration (ASC). Defaults to true.
- ambient_pressure_compensation (Optional, int): Enable compensation of measured CO₂ values based on given ambient pressure in mBar.
- altitude_compensation (Optional, int): Enable compensating deviations due to current altitude (in metres). Notice: setting altitude_compensation is ignored if ambient_pressure_compensation is set.
- address (Optional, int): Manually specify the I²C address of the sensor. Defaults to 0x61.
- update_interval (Optional, Time): The interval to check the sensor. Available range: [2 … 1800]. Defaults to 60s.
## Manual calibration:
# Example on how to implement a UI section in HA for manual calibration.
# Note: Please enter first a CO2 value before pressing the button.
button:
  - platform: template
    name: "SCD30 Force manual calibration"
    entity_category: "config"
    on_press:
      then:
        - scd30.force_recalibration_with_reference:
        value: !lambda 'return id(co2_cal).state;'

number:
  - platform: template
    name: "CO2 calibration value"
    optimistic: true
    min_value: 350
    max_value: 4500
    step: 1
    id: co2_cal
    icon: "mdi:molecule-co2"
    entity_category: "config"
## See Also
- Sensor Filters
- Absolute Humidity
- DHT Temperature+Humidity Sensor
- DHT12 Temperature+Humidity Sensor
- HDC1080 Temperature+Humidity Sensor
- HTU21D | Si7021 | SHT21 Temperature & Humidity Sensor
- API Reference
- Edit this page on GitHub
# Some i2c devices not working after 2025.7.0

## Description
zumbefin
opened
### The problem
Hi, I have SHT40,bme280 and bh1750 connected to esp32. After 2025.7.0 update they remain as unknown devices.
bh1750 gives in log
[W][bh1750.sensor:063]: Set measurement time failed
bme280 gives component mark as failed in some boots and in some it initializes correctly, but does not report any data.
SHT40 works normally.
If I restore the previous version 2025.6.3 everything starts working normally.
The same problem is still in the latest 2025.7.2 version
### Which version of ESPHome has the issue?
2025.7.0
### What type of installation are you using?
Home Assistant Add-on
### What platform are you using?
ESP32
### Component causing the issue
i2c bme280, bh1750
### YAML Config
esphome:
  name: "takapiha-keskus"
  friendly_name: Takapiha-keskus

esp32:
  board: esp32dev
  framework:
    type: arduino

# Enable logging
logger:
  baud_rate: 0

# Enable Home Assistant API
api:
  #encryption:
    #key: "*sensored*"

#mqtt:
  #broker: 10.1.1.5
  #username: takapiha

ota:
  - platform: esphome
    password: *sensored*

safe_mode:
  boot_is_good_after: 90s
  num_attempts: 3

preferences:
  flash_write_interval: 10min

wifi:
  ssid: !secret wifi_ssid
  password: !secret wifi_password

  power_save_mode: none

  # Enable fallback hotspot (captive portal) in case wifi connection fails
  ap:
    ssid: "Takapiha Fallback Hotspot"
    password: "*sensored*"
  fast_connect: off

captive_portal:

#web_server:
  #port: 80
  #version: 3

# i2C pins and setup
i2c:
  sda: GPIO21 # D21
  scl: GPIO22 # D22
  scan: false
  id: bus_a

#co2 kommunikaatio
uart:
  rx_pin: GPIO16
  tx_pin: GPIO17
  baud_rate: 9600

#Valoisuus anturi BH1750
sensor:
  - platform: bh1750
    name: "takapiha valoisuus bh1750"
    address: 0x23
    update_interval: 60s

  - platform: sht4x
    temperature:
      name: "takapiha lämpötila sht40"
      accuracy_decimals: 2
    humidity:
      name: "takapiha kosteus sht40"
      accuracy_decimals: 2
    heater_max_duty: 0.05
    heater_power: High
    heater_time: Long

  - platform: wifi_signal # Reports the WiFi signal strength/RSSI in dB
    name: "WiFi Signal dB"
    id: wifi_signal_db
    update_interval: 60s
    entity_category: "diagnostic"

  - platform: copy # Reports the WiFi signal strength in %
    source_id: wifi_signal_db
    name: "WiFi Signal Percent"
    filters:
      - lambda: return min(max(2 * (x + 100.0), 0.0), 100.0);
    unit_of_measurement: "Signal %"
    entity_category: "diagnostic"
    device_class: ""
#CO2
  - platform: senseair
    co2:
      name: "SenseAir CO2 arvo ulkona"
      accuracy_decimals: 1
    update_interval: 60s

#sisäinen lämpötila
  - platform: internal_temperature
    name: "takapiha ESP lämpötila"

  # BME280 Temperature, Pressure, Humidity sensor
  - platform: bme280_i2c

    temperature:
      name: "takapiha lämpötila bme280"

      accuracy_decimals: 2
    pressure:
      name: "takapiha ilmanpaine bme280"

      accuracy_decimals: 1
      filters:
        - clamp:
        min_value: 930
        max_value: 1070
        ignore_out_of_range: true
    humidity:
      name: "takapiha kosteus bme280"

      accuracy_decimals: 2
    address: 0x76

#restart nappi
switch:
  - platform: restart
    name: "Restart ESP32"
    id: restart_switch

#CO2 lämmittimen rele
  - platform: gpio
    name: "CO2 lämmitys rele"
    pin:
      number: GPIO4
      inverted: true
      mode:
        output: True
        open_drain: True
    restore_mode: ALWAYS_OFF
### Anything in the logs that might be useful for us?
### Additional information
No response
## Activity

### peterd550 commented
peterd550
Try changing the type:
esp32:
board: esp32dev
framework:
type: esp-idf

### zumbefin commented
zumbefin
Author
Bme280 is now working, but bh1750 is giving:
[16:10:22][W][bh1750.sensor:091]: Start measurement failed
[16:10:22][W][component:279]: bh1750.sensor set Warning flag: unspecified
[16:11:22][W][bh1750.sensor:063]: Set measurement time failed
[16:11:22][D][sensor:104]: 'takapiha valoisuus bh1750': Sending state nan lx with 1 decimals of accuracy

### peterd550 commented
peterd550
I have resolved my issue.
A simple reboot of my home assistant and cleaned my build and install.
It did a heap of pip install's and compiling but it works now :)
ssieb
closed this as not planned
ssieb
reopened this

### zumbefin commented
zumbefin
Author
Not helping for me i did a build clean and full restart to ha bh1750 still not working.

### ssieb commented
ssieb
Member
Need to see serial logs from boot.

### botvos5 commented
botvos5
· edited by botvos5
AHT20 i2c doesnt work either. I2C scan fails with AHT20 sensor after the update. No HW changes made. Its an ESP32 Drvkit V1.
[08:46:51][I][i2c.arduino:100]: Results from bus scan:
[08:46:51][E][i2c.arduino:108]: Unknown error at address 0x08
[08:46:51][E][i2c.arduino:108]: Unknown error at address 0x09
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x0A
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x0B
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x0C
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x0D
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x0E
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x0F
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x10
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x11
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x12
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x13
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x14
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x15
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x16
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x17
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x18
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x19
[08:46:52][E][i2c.arduino:108]: Unknown error at address 0x1A